Vincenti:

1. Fix the Bridge origin and Orientation in GPS frame.
2. Fix the position of inspector (in GPS coordinates), and orientation of IFR (roll, pitch and yaw).
3. Compute the IFR origin w.r.t. BFR.
  a) Using Inspector origin and Bridge origin in GPS, get the distance and elevation change (applying Vincenti algorithm).
  b) This vector is then projected in BFR to get the Inspector position in BFR.
4. Also compute the orientation of IFR w.r.t. BFR.
  a) Subtract orientation values in BFR (w.r.t. GPS) from the orientation values in IFR (w.r.t. GPS).
5. Set the Near Plane Distance, Far Plane Distance, and viewing angle, within which the region of interest falls (w.r.t. IFR).
6. Compute the bounding box parameters.
  a) Compute the near plane distance in BFR using the same point in IFR, inspector origin w.r.t. BFR, and orientation of inspector w.r.t. BFR.
  b) Repeat above step for far plane distance.
7. Containment Algorithm -
  a) Iterate through every node on bridge (in BFR).
  b) Check if point in 7(a) lies within the bounding box (determined using parameters specified by the user).
  c) Required values for above step – Inspector position, near plane, far plane distance and query point, all in BFR.
Approximate Algorithm:

1. Determine the origin of the bridge:
  a) Enter the GPS and BFR coordinates of 4 points on the Bridge.
  b) Use these points to compute BG matrix and Scaling factors.
  c) Now we can compute the Bridge origin using BG matrix and the 4 points on the Bridge
2. Enter the Inspector position and orientation (i.e. roll, pitch and yaw) in GPS frame.
3. Also enter the Near Plane and Far Plane distances in IFR, along with the view angle.
4. Compute the bounding box parameters
  a) Near Plane Distance point in BFR using BG and IG matrices (computed using roll, pitch and yaw of the inspector)
  b) Similarly compute the Far Plane Distance point and Inspector position in BFR from the above.
5. Containment Algorithm -
  a) Iterate through every node on bridge (in BFR).
  b) Check if point in 5(a) lies within the bounding box (determined using parameters specified by the user).
  c) Required values for above step – Inspector position, near plane, far plane distance and query point, all in BFR.

For Error analysis:
1. In Approximate algorithm, we compute the error in inspector position by sampling values from Weibull distribution. This is done by sampling distance error from the distribution, and then multiplying it with a random orientation angle of the distance vector.
2. In Vincenti, once we get the distance error vector, we use Vincenti algorithm to compute the new position of the inspector (with the error).

MATLAB:

Given all the bridge node points in BFR, Input the position of inspector in BFR, near plane, far plane distance and angle of view.
     The Far plane distance point is (0,0,0) and the near plane distance point is the position of	inspector divided by 2.
  1. Determine euclidean distance of inspector from the Near and Far plane points.
  2. Iterate through every node in the Bridge-
    a) Determine distance of node from the Inspector position.
    b) Determine phi, which is the half angle of the visual cone.
    c) Check for containment of node in the visual cone.