Global Positioning Systems are used widely in the Structural Engineering community as navigation sensors. GPS sensors provide accurate latitude, longitude and altitude coordinates for the location of GPS receiver anywhere on Earth. GPS works using satellites that are continuously orbiting the Earth at 2 rotations/day, to ensure that at any time and any point on Earth, at least 4 satellites are visible in the sky. The GPS receiver locates these satellites, figures out its distance from the 4 satellites, and uses trilateration to deduce its own location. However several factors like atmospheric conditions (GPS signals are refracted in atmosphere), ephemeris errors/clock drift, measurement noise and multi-path(GPS signals bouncing off reflective surfaces and reaching receivers) result in errors in GPS positions. These GPS position errors can be modeled by a Weibull distribution with b=2.

Having designed and implemented a spatial context interpretation framework for extracting sensor nodes within a region of interest defined by the inspector position/orientation (spatial context), we now analyze the effect of GPS errors and how it would affect the element identification accuracy in the framework. We design the typical path of an inspector who is on an inspection routine, by picking inspector positions at intervals of 40 feet. We determine these positions in Bridge Frame of Reference (BFR). We also determine the inspector's orientation in each of these positions (which would be given by orientation sensors), by setting roll, pitch and yaw to values that would allow the inspector's visual cone to contain sensor nodes on the bridge. So we now have discretized the path of the inspector, and defined his spatial context during an inspection routine of the bridge.

Before beginning the simulation, we now have the following information about the bridge/inspector:
1. Locations of all the sensor nodes on the bridge (in BFR)
2. Mapping of every sensor node to an element on the bridge.
3. Since an inspector who is moving above the bridge, would not be able to view sensor nodes below the deck and vice-versa, we create element visibility table for visible elements above and below the deck. The boundary/deck position is chosen to be 19 feet for our case study of Telegraph Bridge.
4. Based on element visibility mapping obtained from Step 3, we split the sensor nodes list in Step 1, to obtain sensor nodes above and below the bridge. This is done to optimize our framework.
5. 128 different positions of the inspector in BFR, along with roll, pitch and yaw values for each position.

Once we have the above input data for simulation, we begin by reading the file containing spatial context information of inspection path in BFR. For each such context, record the 'true' inspector position in BFR. We then generate 100 error samples for the inspector's position, from Weibull distribution with beta=2. Each error sample is added to the current inspector's position in BFR, to obtain 'observed' inspector position.

Similarly we simulate the 'observed' orientation of the inspector, which would be different from the 'true' orientation because of errors in device measuring orientation. This error is not very large, and so we restrict it to a value between -0.5 degree and 0.5 degree.

Once we have the 'observed' spatial context of inspector (i.e. 'observed' position/orientation), we now determine the near and far plane points for the inspector in BFR. We have taken the near and far plane distances to be 3 feet to 30 feet along with a view angle of 30 degrees, considering the visual cone of interest for the human eye. Thus the data would help us determine the near and far plane points of the current inspector position in BFR.

Having defined the visual cone of interest for the inspector and depending on the inspectors position relative to the deck, we parse the appropriate file of element nodes above/below deck. For each element node, we check if it is contained within the bounding box of the inspector. If the condition evaluates to true, we record the element to which the node belongs.

At the end of the above program, we have a list elements identified along with the fraction of element nodes that fall within the bounding box, for every 'observed' spatial context of inspector in BFR. For analyzing element identification accuracy in 'observed' spatial context, we would require information similar information about elements identified for every 'true' spatial context of inspector. Thus we repeat the above sequence of steps, for each 'true' spatial context of inspector i.e. without errors.

At this stage we have obtained results for 'observed' inspector positions and corresponding 'true' position, which would allow us to make inferences about element identification accuracy. To do this,
we parse the output files for 'observed' positions, and determine percentage of correctly identified elements in all 'observed' positions relative to the corresponding 'true' position. We also determine elements identified in 'observed' positions, that were not obtained in the corresponding 'true' position (i.e. False Positives). Similarly we record element identification percentages for elements in true position, that were not identified in any of the corresponding observed positions i.e. False Negatives.

We now have the percentages for elements identified correctly along with false positives and false negatives for every inspector position. We use these results to obtain the probability of an element being missed on average, for any position of inspector on the bridge.
A brief summary of the algorithm:
define NUM_OF_RUNS 5
for runs=1 to NUM_OF_RUNS
  for each inspector position
    1. Set the 'true' inspector position in BFR
    2. for each sampled error distance value from Weibull Distribution
      1. Obtain error distance sample from the distribution if above deck and set to 0.5 m if below deck
      2. Generate a random orientation angle for error vector.
      3. Compute 'observed' inspector position in BFR by adding error vector (obtained from magnitude and orientation in Step 1 and 2) to 'true' inspector position
      4. Add errors in roll, pitch and yaw (randomly generated between -0.5 and 0.5) to the roll, pitch and yaw values for current 'true' orientation of inspector
      5. Determine the Near and Far plane points in BFR, using 'observed' inspector position and distance of the respective planes from the inspector.
      6. The inspector position in BFR, near and far plane points, along with the view angle determine the bounding box/region of interest of the inspector.
      7. Compute all nodes within the bounding box of the inspector.
        1. Depending on whether the inspector is above or below the deck, choose the corresponding list of element nodes to parse.
        2. Check if each element node is contained in the bounding box.
        3. Record percentage of element nodes identified for every element that falls in bounding box of inspector